## Slide 1
Instruments for Natural Radiation Detection:
Educating the public using inexpensive muon detectors
J. Hanania and J.M.K.C. Donev
Conclusion
We would like to thank the Canadian Nuclear Society for the funding of this project.
United Nations Scientific Committee on the Effects of Atomic Radiation (2008). “Sources and effects of ionizing radiation”, UNSCEAR 2008 Report. New York: United Nations (published 2010).
E. Aguayo et al., “Cosmic Ray Interactions in Shielding Materials", United States Department of Energy, prepared by Pacific Northwest National Labs, 2011
S. Axani, J. Conrad, and C. Kirby, “The Desktop Muon Detector: A simple, physics-motivated machine- and electronics-shop project for university students”. Massachusetts Institute of Technology (2016).
References
Overview
Cosmic muons bombard Earth’s surface from space, contributing to natural radiation doses
The average Canadian receives around 20% of their natural radiation dose from cosmic rays, which include muons.
Due to ionizing properties, muons can be detected easily.
Constructed two muon detectors for use as educational tools
Capabilities:
Record time of muon event
Distinguish between high and low energy muons
Generate histogram of count rates and energies
Small and lightweight
Low operating voltage (5V)
Cost per unit
~ $400CAD
Figure 1. Muon detectors were built from scratch, shown to be about the size of a hand.
Shielding experiment: Determined that ~0.9 m of concrete is above UCalgary Physics basement
Figure 3. Muon count rates taken inside and outside UofC physics basement determined presence of concrete (estimated using data from [Ref 2]).
How Muons are Detected
Scintillation: Muon produces photons
Light detection: Photons produce electrical signal
μ
Muon
Plastic scintillator
Photons
Signal processing: Circuitry amplifies and extends signal so it can be measured by a computer
6 mm
Silicon photomultiplier
Photons
t
V
Electrical signal
t
V
Circuitry
These portable muon detectors can operate just about anywhere, requiring only a laptop connection. Various experiments can be performed, with many educational opportunities in particle physics, nuclear physics, and special relativity. Moreover, these detectors can be reproduced by a dedicated undergraduate student or teacher at low cost.
Educational uses
Many possible educational uses, including:
Passive demonstration: gives observer knowledge of and appreciation for the presence of muons
Experimentation:
  Special Relativity test
  Muon shielding from various materials
  High elevation tests
Instrument construction: valuable experience gained in the building of such an instrument
Canada-wide muon project: educators from around Canada build their own instruments on their own or with a class
# of detectors | 1 | 100
Cost per detector (CAD) | $392 | $126
Table 1. Cost per detector unit; values are approximate as shipping costs may vary and fewer/extra components may be needed
Figure 3. Natural radiation dose by source received by the average Canadian per year.
Easily repeated using other materials like wood, aluminum, or lead.
Top of troposphere
Muon
Figure 2. Showers of cosmic particles occur ~15 km above sea level